## Slide 1
COMPUTER NETWORKS • UNIT I
OSI and TCP/IP
Reference Models
Layers and Their Functions • Comparison of the Two Models
Reference Textbooks: TB1 — Tanenbaum, Feamster & Wetherall, "Computer Networks", 6th Ed.
TB2 — Behrouz A. Forouzan, "Data Communications and Networking", 5th Ed.

## Slide 2
ROADMAP
What We'll Cover
1
Why a Layered Model?
The idea behind dividing network tasks into layers
2
The OSI Model
Seven layers, from physical bits to user applications
3
OSI Layers 1–4
Physical, data link, network & transport in detail
4
OSI Layers 5–7
Session, presentation & application layers
5
The TCP/IP Model
The protocol suite that actually runs the Internet
6
TCP/IP Layers & Protocols
Mapping real protocols to each layer
7
Data Encapsulation
How a message becomes bits, layer by layer
8
OSI vs. TCP/IP
Mapping the two models & comparing them
Unit I — OSI & TCP/IP Reference Models
2

## Slide 3
FOUNDATIONS
Why a Layered Model?
Network communication is a complex task. Instead of solving it as one giant problem, it is divided into several smaller, manageable layers — each layer handling one part of the job.
Key Design Principles
Each layer performs a specific, well-defined set of duties
A layer offers services to the layer above it, and uses services from the layer below it
Well-defined interfaces exist between adjacent layers
A change inside one layer should not require changes in other layers
Layer 3
Layer 3
Layer 2
Layer 2
Layer 1
Layer 1
Sender
Receiver
Physical medium (actual communication path)
Unit I — OSI & TCP/IP Reference Models
3

## Slide 4
THE OSI MODEL
Seven Layers, One Framework
Developed by ISO (International Organization for Standardization), the Open Systems Interconnection model is a reference framework describing how information moves from one device, through a network, to another.
7
Application
6
Presentation
5
Session
4
Transport
3
Network
2
Data Link
1
Physical
Layer 7 is closest to the end user; Layer 1 is closest to the physical medium.
Mnemonic:
"All People Seem To
Need Data Processing"
(Application → Physical)
Unit I — OSI & TCP/IP Reference Models
4

## Slide 5
OSI MODEL — LAYER 1
Layer 1: Physical Layer
1
PHYSICAL LAYER
OSI Layer 1
Coordinates the functions required to transmit a raw bit stream over a physical medium — concerned purely with bits, not their meaning.
Bit Representation
Encodes bits (0s and 1s) into electrical or optical signals
Data Rate
Defines the transmission rate — the number of bits sent per second
Synchronization
Synchronizes the sender’s and receiver’s clocks at the bit level
Line Configuration
Connects devices via a point-to-point or multipoint link
Physical Topology
Defines how devices are arranged — mesh, star, bus, ring, or hybrid
Transmission Mode
Defines the direction of flow — simplex, half-duplex, or full-duplex
Unit I — OSI & TCP/IP Reference Models
5

## Slide 6
OSI MODEL — LAYER 2
Layer 2: Data Link Layer
2
DATA LINK LAYER
OSI Layer 2
Transforms the physical layer’s raw transmission facility into a reliable link; responsible for node-to-node (hop-to-hop) delivery.
Framing
Divides the bit stream from the network layer into manageable frames
Physical Addressing
Adds a header with sender/receiver physical (MAC) addresses
Flow Control
Prevents a fast sender from overwhelming a slower receiver
Error Control
Adds mechanisms to detect and retransmit damaged or lost frames
Access Control
Determines which device controls the link at any given time
Unit I — OSI & TCP/IP Reference Models
6

## Slide 7
OSI MODEL — LAYER 3
Layer 3: Network Layer
3
NETWORK LAYER
OSI Layer 3
Responsible for the source-to-destination delivery of a packet, possibly across multiple, independent networks (routers/links).
Logical Addressing
Adds a header with the logical (e.g., IP) addresses of sender & receiver, distinct from physical addresses
Routing
Connects independent networks (routers) to form an internetwork, and determines the best path for each packet
Unit I — OSI & TCP/IP Reference Models
7

## Slide 8
OSI MODEL — LAYER 4
Layer 4: Transport Layer
4
TRANSPORT LAYER
OSI Layer 4
Responsible for process-to-process (program-to-program) delivery of the entire message, ensuring it arrives intact and in order.
Service-Point Addressing
Adds a header with a port number to deliver data to the correct process on the destination host
Segmentation & Reassembly
Divides a message into transmittable segments, each numbered for reassembly at the destination
Connection Control
Can be connection-oriented or connectionless
Flow & Error Control
Performed end-to-end (source to destination), rather than link-by-link
Unit I — OSI & TCP/IP Reference Models
8

## Slide 9
OSI MODEL — LAYERS 5, 6 & 7
Session, Presentation & Application
5
Session Layer
Dialog control — allows two systems to communicate in half- or full-duplex mode
Synchronization — adds checkpoints into a stream of data for recovery
6
Presentation Layer
Translation — converts between different data representations / encodings
Encryption & decryption — for privacy and security
Compression — reduces the number of bits to be transmitted
7
Application Layer
Enables users to access the network via services like e-mail, file transfer, and remote login
Provides user interfaces and support for services such as directories and file/database access
Unit I — OSI & TCP/IP Reference Models
9

## Slide 10
THE TCP/IP MODEL
Overview of the Protocol Suite
TCP/IP predates the OSI model. It was developed by DARPA for use in ARPANET, the forerunner of today’s Internet, so it is often called the Internet model. Unlike OSI, it is an actual, working protocol suite — not just a reference framework.
The classic model has four layers; a common five-layer version aligns it more closely with OSI by separating the network access layer into physical and data link layers.
Application
Transport
Internet (Network)
Data Link
Physical
Sometimes combined into a single "Network Access" layer (classic 4-layer view)
Unit I — OSI & TCP/IP Reference Models
10

## Slide 11
THE TCP/IP MODEL
Layers & Key Protocols
Application
Combines OSI’s session, presentation & application layers; supports process-to-process communication
HTTP, FTP, SMTP, DNS, Telnet, SNMP
Transport
Provides end-to-end message delivery, with or without reliability guarantees
TCP, UDP, SCTP
Internet
Handles logical addressing and routing of packets across networks
IP, ICMP, IGMP, ARP
Data Link / Network Access
Handles the physical transmission of data over the local network medium
Ethernet, PPP, Wi-Fi (802.11), Frame Relay
Unit I — OSI & TCP/IP Reference Models
11

## Slide 12
MOVING DATA THROUGH THE LAYERS
Data Encapsulation
As data moves down through the layers at the sender, each layer adds its own header (and sometimes a trailer) — wrapping the data from the layer above.
Application
Message
Transport
H1
Segment
Internet
H2
Packet / Datagram
Data Link
H3
Frame
Physical
H4
Bits
Each layer’s header (H1, H2, H3…) carries the control information that layer needs — e.g., the transport header carries port numbers, the network header carries IP addresses.
At the receiver, the reverse process — decapsulation — strips each header away, layer by layer, until the original message is recovered.
Unit I — OSI & TCP/IP Reference Models
12

## Slide 13
COMPARING THE TWO MODELS
OSI vs. TCP/IP — Layer Mapping
Application
Presentation
Session
Transport
Network
Data Link
Physical
OSI Model (7 layers)
Application
Transport
Internet
Network Access
TCP/IP Model (4 layers)
Unit I — OSI & TCP/IP Reference Models
13

## Slide 14
COMPARING THE TWO MODELS
Similarities & Differences
Similarities
Both are built on the concept of a stack of independent layers
Both have comparable Network and Transport layers performing similar roles
Both assume that packets are switched — a device may use different routes to reach the same destination
Knowledge of one model makes the other easier to understand
Differences
OSI has 7 layers; TCP/IP has 4 (or 5, in the expanded view)
OSI is a generic, protocol-independent reference model; TCP/IP is an actual, implemented protocol suite
OSI was developed by ISO; TCP/IP by DARPA, ahead of OSI
OSI separates session & presentation as distinct layers; TCP/IP folds them into the application layer
TCP/IP is what the real Internet runs on today; OSI’s protocols never saw wide adoption
Unit I — OSI & TCP/IP Reference Models
14

## Slide 15
KEY TAKEAWAYS
OSI & TCP/IP, at a Glance
Layered design
Networking tasks are split into independent layers, each with well-defined duties and interfaces.
OSI’s 7 layers
Physical, Data Link, Network, Transport, Session, Presentation & Application — a complete reference model.
TCP/IP’s layers
Application, Transport, Internet & Network Access — the suite the real Internet actually runs on.
Encapsulation
Each layer wraps data from above with its own header, forming messages, segments, packets, frames & bits.
Model comparison
OSI is a conceptual reference; TCP/IP is a practical, implemented protocol suite with fewer, broader layers.
Real-world routing
Both models assume a packet-switched network where routing decisions can vary per packet.
Unit I — OSI & TCP/IP Reference Models
15

## Slide 16
BIBLIOGRAPHY
References
Text Books
TB1. A. S. Tanenbaum, N. Feamster & D. J. Wetherall, "Computer Networks," Pearson Education, 6th Edition, 2021.
TB2. Behrouz A. Forouzan, "Data Communications and Networking," 5th Edition, McGraw-Hill Education, 2013.
Reference Books
RB1. D. E. Comer, "Internetworking with TCP/IP, Volume 1: Principles, Protocols, and Architecture," Pearson, 6th Ed., 2014.
RB2. William Stallings, "Data and Computer Communications," Pearson Education, 11th Edition, 2023.
RB3. A. Leinwand & B. Pinsky, "Cisco Router Configuration Handbook," 2nd Edition, Cisco Press, 2001.
Unit I — OSI & TCP/IP Reference Models
16