## Slide 1
COMPUTER NETWORKS • UNIT I
Basic Concepts of
Data Communication
Components • Distributed Processing • Line Configuration • Topology • Transmission Mode • Categories of Networks
Reference Textbooks: TB1 — Tanenbaum, Feamster & Wetherall, "Computer Networks", 6th Ed.
TB2 — Behrouz A. Forouzan, "Data Communications and Networking", 5th Ed.

## Slide 2
ROADMAP
What We'll Cover
1
Data Communication
Definition, effectiveness criteria & network criteria
2
Components
The five elements of a communication system
3
Distributed Processing
Why tasks are split across multiple computers
4
Line Configuration
Point-to-point vs. multipoint connections
5
Network Topology
Mesh, star, bus, ring & hybrid layouts
6
Transmission Mode
Simplex, half-duplex & full-duplex
7
Categories of Networks
LAN, MAN & WAN compared
Unit I — Basic Concepts of Data Communication
2

## Slide 3
FOUNDATIONS
What Is Data Communication?
Data communication is the exchange of data between two devices via some form of transmission medium such as a wire cable.
For communication to occur, the devices must be part of a communication system made up of a combination of hardware and software.
4
The effectiveness of a data communication system depends on these four fundamental characteristics — each one shown on the right.
Delivery
Data must be delivered to the correct destination — only the intended device or user should receive it.
Accuracy
Data must be delivered accurately; altered data during transmission is unusable.
Timeliness
Data must be delivered in a timely manner. Late data is useless (e.g., real-time audio/video).
Jitter
Jitter is the variation in packet arrival time, causing uneven quality in audio/video delivery.
Unit I — Basic Concepts of Data Communication
3

## Slide 4
FOUNDATIONS
Network Criteria
A network must be evaluated against three essential criteria to be considered effective and useful.
Performance
Measured by transit time (time for a message to travel) and response time (time between a request and its response). Evaluated using throughput and delay.
Reliability
Measured by frequency of failure, the recovery time of a network after a failure, and the network’s robustness in a catastrophe.
Security
Protecting data from unauthorized access, damage-proofing data against errors, and implementing policies for recovery from breaches.
Unit I — Basic Concepts of Data Communication
4

## Slide 5
COMPONENTS OF DATA COMMUNICATION
The Five Elements of a System
Message
The information (data) to be communicated. Popular forms include text, numbers, pictures, audio, and video.
Sender
The device that sends the data message — a computer, workstation, telephone, video camera, and so on.
Receiver
The device that receives the message — a computer, workstation, telephone, television, and so on.
Transmission Medium
The physical path by which a message travels from sender to receiver — twisted-pair wire, coaxial cable, fiber-optic cable, or radio waves.
Protocol
A set of rules that govern data communication; represents an agreement between communicating devices — without it, two devices may be connected but not communicating.
Unit I — Basic Concepts of Data Communication
5

## Slide 6
COMPONENTS OF DATA COMMUNICATION
How the Five Elements Interact
PROTOCOL — the agreed set of rules that governs the exchange of data between sender and receiver
SENDER
TRANSMISSION
MEDIUM
RECEIVER
MESSAGE
The sender encodes the message and transmits it across the medium, following the shared protocol, until it is decoded correctly by the receiver.
Unit I — Basic Concepts of Data Communication
6

## Slide 7
NETWORK DESIGN CONCEPTS
Distributed Processing
Most networks use distributed processing, in which a task is divided among multiple computers. Instead of a single large machine handling every job for a group, separate, smaller computers—typically one per user—each handle a portion of the task.
Advantages
Security / encapsulation — a system can be attacked at only one access point, isolating sensitive data on a specific machine.
Faster problem solving — multiple computers working on parts of a problem finish faster than one machine alone.
Security through distributed databases — reduces the catastrophic effect of losing all data at a single site.
Collaborative processing — one computer can request, and even provide, services from another.
One task, shared across independent computers
Unit I — Basic Concepts of Data Communication
7

## Slide 8
PHYSICAL CONNECTION
Line Configuration
Line configuration refers to the way two or more communication devices attach to a physical link. There are two possible line configurations:
Point-to-Point
A dedicated link is established between exactly two devices. The entire capacity of the link is reserved for transmission between those two devices only.
Example: microwave / satellite links, remote-control infrared links
Multipoint (Multidrop)
More than two specific devices share a single link. The capacity of the channel is shared, either spatially (simultaneous use) or temporally (users take turns).
Unit I — Basic Concepts of Data Communication
8

## Slide 9
NETWORK TOPOLOGY
What Is a Network Topology?
Topology refers to the physical or logical arrangement of a network — how devices (nodes) and connecting lines (links) are laid out. There are five basic topologies:
Mesh
Every device has a dedicated link to every other device
Star
Every device has a link to a central hub only
Bus
All devices share a single backbone cable
Ring
Each device connects to exactly two neighbors, forming a loop
Hybrid
A combination of two or more basic topologies
A network combines two or more different topologies to form a hybrid topology.
Unit I — Basic Concepts of Data Communication
9

## Slide 10
NETWORK TOPOLOGY
Mesh Topology
n(n−1)/2 dedicated links for n devices
Every device has a dedicated point-to-point link to every other device in the network. A fully connected mesh with n nodes requires n(n−1)/2 physical links and n−1 I/O ports per device.
Advantages
• Eliminates traffic problems of shared links
• Robust — link failure disables only one connection
• Privacy / security between devices
• Easy fault identification & isolation
Disadvantages
• High cabling & I/O port requirements
• Expensive to install and reconfigure
• Bulky wiring, hard to maintain
• Best suited for small / critical networks
Unit I — Basic Concepts of Data Communication
10

## Slide 11
NETWORK TOPOLOGY
Star Topology
Central hub / switch controls all data traffic
Each device has a dedicated point-to-point link only to a central controller, usually called a hub. Devices are not directly linked to one another — the hub acts as an exchange, relaying data between them.
Advantages
• Less expensive than mesh (one link/device)
• Easy to install and reconfigure
• Robustness — one link failure affects only that device
• Simple fault identification
Disadvantages
• Depends entirely on the hub
• Hub failure brings down the whole network
• More cabling than bus/ring topologies
Unit I — Basic Concepts of Data Communication
11

## Slide 12
NETWORK TOPOLOGY
Bus Topology
Single shared backbone cable (with terminators at each end)
One long cable acts as a backbone to link all the devices in the network. Nodes connect via drop lines and taps; a signal from any device travels the length of the medium in both directions.
Advantages
• Easy installation; less cabling than mesh/star
• Backbone lays out along the shortest path
Disadvantages
• Difficult reconnection & fault isolation
• A break in the cable can stop all transmission
• Signal reflection at taps causes degradation
Unit I — Basic Concepts of Data Communication
12

## Slide 13
NETWORK TOPOLOGY
Ring Topology
Each device (repeater) connects to exactly two neighbors
Each device has a dedicated point-to-point link with only the two devices on either side of it. A signal is passed along the ring, in one direction, until it reaches its destination; each device regenerates the signal it receives.
Advantages
• Relatively easy to install & reconfigure
• Fault isolation is simplified
Disadvantages
• Unidirectional traffic; a break can disable the whole ring
• Dual ring / switch needed for resilience
Unit I — Basic Concepts of Data Communication
13

## Slide 14
NETWORK TOPOLOGY
Hybrid Topology
A hybrid topology combines two or more different basic topologies. It is designed to capitalize on the strengths of each while minimizing their individual weaknesses.
Example: a large organization might connect several star-topology LANs in different departments to a common bus backbone — combining the star’s manageability with the bus’s efficient backbone.
Star clusters joined by a common bus backbone
Unit I — Basic Concepts of Data Communication
14

## Slide 15
DIRECTION OF DATA FLOW
Transmission Mode
Communication between two devices can be one of three types, based on the direction of signal flow.
Simplex
Communication is unidirectional — only one device can transmit; the other can only receive. The entire capacity of the channel is used in one direction.
Example: keyboards and monitors (keyboard only sends, monitor only receives).
Half-Duplex
Each device can both transmit and receive, but not at the same time — when one sends, the other can only receive, and vice versa.
Example: walkie-talkies, CB (citizens band) radios.
Full-Duplex
Both devices can transmit and receive simultaneously; the channel capacity is divided (or doubled) to allow signals in both directions at once.
Example: telephone networks — both parties can talk and listen at the same time.
Unit I — Basic Concepts of Data Communication
15

## Slide 16
CATEGORIES OF NETWORKS
Local Area Network (LAN)
A LAN interconnects devices within a single office, building, or campus, and is normally privately owned by the organization that uses it.
Restricted in size, spanning up to a few kilometers
Data rates typically range from a few Mbps to several Gbps
Designed to share resources — hardware, software, or data — among PCs/workstations
Often uses a single shared or switched medium (e.g., Ethernet)
Distinguished from other networks by size, transmission technology, and topology
Single Building / Campus
Unit I — Basic Concepts of Data Communication
16

## Slide 17
CATEGORIES OF NETWORKS
Metropolitan & Wide Area Networks
MAN
Metropolitan Area Network
A network with a size between a LAN and a WAN, normally covering an entire city. It may be a single network (e.g., a cable TV network) or connect a number of LANs into a larger network.
Owned by a private company or a public utility
Spans a city or large campus complex
Example: local telephone company networks, city cable TV
WAN
Wide Area Network
Provides long-distance transmission of data over large geographic areas — a country, a continent, or even the whole world — often using links provided by common carriers.
Two types: switched and point-to-point WANs
Interconnects intermediate nodes (routers/switches)
Example: the Internet backbone; large corporate networks
LAN < MAN < WAN — as geographic scope grows, ownership shifts from private (LAN) to shared/public infrastructure (WAN).
Unit I — Basic Concepts of Data Communication
17

## Slide 18
KEY TAKEAWAYS
Unit I — Basic Concepts, at a Glance
Data communication
Needs a message, sender, receiver, medium & protocol, and is judged by delivery, accuracy, timeliness & jitter.
Distributed processing
Splits tasks across smaller, cooperating computers for speed, security, and resilience.
Line configuration
Devices connect either point-to-point (dedicated) or multipoint (shared).
Topology
Mesh, star, bus, ring & hybrid — each trades off cost, reliability and scalability differently.
Transmission mode
Simplex, half-duplex, and full-duplex describe the direction of data flow.
Categories of networks
LAN, MAN and WAN differ mainly by geographic scope and ownership.
Unit I — Basic Concepts of Data Communication
18
18

## Slide 19
BIBLIOGRAPHY
References
Text Books
TB1. A. S. Tanenbaum, N. Feamster & D. J. Wetherall, "Computer Networks," Pearson Education, 6th Edition, 2021.
TB2. Behrouz A. Forouzan, "Data Communications and Networking," 5th Edition, McGraw-Hill Education, 2013.
Reference Books
RB1. D. E. Comer, "Internetworking with TCP/IP, Volume 1: Principles, Protocols, and Architecture," Pearson, 6th Ed., 2014.
RB2. William Stallings, "Data and Computer Communications," Pearson Education, 11th Edition, 2023.
RB3. A. Leinwand & B. Pinsky, "Cisco Router Configuration Handbook," 2nd Edition, Cisco Press, 2001.
Unit I — Basic Concepts of Data Communication
19