## Slide 1
TRANSMISSION MEDIA
Guided & Unguided Media, Signal Impairments
and Channel Capacity
Attenuation • Distortion • Noise • S/N Ratio • Throughput • Propagation • Wavelength • Shannon Capacity

## Slide 2
02
FUNDAMENTALS
Introduction to Transmission Media
The physical path along which a signal travels from transmitter to receiver.
Positioned below the physical layer and directly controlled/guided by it.
Two broad categories:
  Guided media – wired, signal travels through a solid conductor.
  Unguided media – wireless, signal travels through free space.
Quality and performance depend on characteristics of the medium and of the signal itself.
Choice of medium affects bandwidth, cost, distance, and susceptibility to interference.
Data Communication Fundamentals

## Slide 3
03
WIRED TRANSMISSION
Guided Media – Overview
Also called “bound media” – they provide a physical conduit from one device to another.
The signal is confined and directed within the physical limits of the medium.
Metallic conductors (twisted-pair, coaxial cable) transmit signals as electric current.
Fiber-optic cable transmits signals as pulses of light through glass or plastic.
Generally offer higher reliability and security than wireless media over short-to-medium distances.
Performance is measured by bandwidth, attenuation, and immunity to interference.
Guided Media

## Slide 4
04
WIRED TRANSMISSION
Guided Media – Types
Twisted-Pair Cable
  Two insulated copper wires twisted together to reduce electrical interference and crosstalk.
  Common in telephone lines and LANs (UTP / STP).
Coaxial Cable
  Central copper conductor, insulating layer, metallic shield, and outer jacket.
  Higher bandwidth than twisted pair; used in cable TV and early Ethernet networks.
Fiber-Optic Cable
  Glass or plastic core carrying light signals; very high bandwidth and very low attenuation.
  Immune to electromagnetic interference; used for backbone and long-haul networks.
Guided Media

## Slide 5
05
WIRELESS TRANSMISSION
Unguided Media – Overview
Also called “wireless media” – transport electromagnetic waves without a physical conductor.
Signals are broadcast through air, free space, or water and are available to anyone able to receive them.
No physical boundary directs the signal, so propagation depends on the frequency used.
Three propagation modes:
  Ground propagation – low-frequency waves travel near the earth’s surface.
  Sky propagation – higher-frequency waves reflect off the ionosphere.
  Line-of-sight propagation – very high-frequency waves travel in a straight line.
Unguided Media

## Slide 6
06
WIRELESS TRANSMISSION
Unguided Media – Types
Radio Waves
  Omnidirectional and can penetrate walls; used for AM/FM radio and cordless phones.
Microwaves
  Unidirectional, require line-of-sight antennas; used for satellite and terrestrial links.
Infrared
  Short-range, line-of-sight only, cannot pass through walls; used in remote controls.
Unguided Media

## Slide 7
07
SIGNAL IMPAIRMENT
Attenuation
Loss of signal strength (energy) as it travels through a transmission medium.
Caused by the resistance of the medium; increases with distance travelled.
Measured in decibels (dB):
  dB = 10 × log₁₀ (P₂ / P₁), where P₁ and P₂ are signal power at two points.
A negative dB value indicates loss (attenuation); a positive value indicates gain (amplification).
Compensated using amplifiers in analog systems and repeaters in digital systems.
Signal Impairments

## Slide 8
08
SIGNAL IMPAIRMENT
Distortion
A change in the shape or form of a signal as it travels through the medium.
Mainly affects composite signals made up of several different frequencies.
Each frequency component travels at a slightly different propagation speed through the medium.
Components arrive at the receiver at different times, altering the overall shape of the signal.
This delay-based effect (delay distortion) is common in wired transmission media.
Signal Impairments

## Slide 9
09
SIGNAL IMPAIRMENT
Noise
Unwanted electrical or electromagnetic energy that degrades the quality of a signal.
Thermal noise
  Random motion of electrons in a conductor; present in all electronic devices.
Induced noise
  Comes from sources such as motors and appliances that act like a sending antenna.
Crosstalk noise
  The effect of one wire on another due to electromagnetic coupling.
Impulse noise
  Sudden spikes from power lines, lightning, or switching equipment.
Signal Impairments

## Slide 10
10
SIGNAL QUALITY
Signal-to-Noise Ratio (S/N)
A measure of signal quality – the ratio of signal power to noise power at a point.
SNR = Average signal power / Average noise power
Often expressed in decibels: SNR(dB) = 10 × log₁₀ (SNR)
A high SNR means the signal is strong relative to noise – a clean, reliable channel.
A low SNR means noise is comparable to (or stronger than) the signal, causing errors.
SNR is a key input to the Shannon capacity formula, which sets the maximum achievable data rate.
Channel Performance

## Slide 11
11
CHANNEL PERFORMANCE
Throughput
A measure of how fast data can actually pass through a link or network.
Defined as the number of bits that can pass a given point in one second.
Throughput vs. Bandwidth:
  Bandwidth is a potential measurement – the theoretical capacity of the medium.
  Throughput is an actual measurement – what is really achieved in practice.
In practice, throughput is always less than or equal to bandwidth.
Affected by network congestion, device processing limits, and medium quality.
Channel Performance

## Slide 12
12
SIGNAL TRAVEL
Propagation Speed and Time
Propagation speed
  The rate at which a signal travels through a medium; depends on the medium and frequency.
  Close to the speed of light in air; slower in copper and fiber-optic cable.
Propagation time
  The time required for a signal to travel from sender to receiver.
  Propagation time = Distance / Propagation speed
Longer distances or slower media increase propagation time and, in turn, overall delay.
Signal Travel

## Slide 13
13
SIGNAL TRAVEL
Wavelength
The distance a simple signal travels in one period (one complete cycle).
Links propagation speed to the frequency of a signal in a given medium.
Wavelength = Propagation speed / Frequency (λ = v / f)
Usually measured in micrometers for light travelling through fiber optics.
Measured in meters for radio waves travelling through air or vacuum.
Higher frequency corresponds to shorter wavelength, and vice versa.
Signal Travel

## Slide 14
14
CHANNEL CAPACITY
Shannon Capacity
Defines the theoretical maximum data rate achievable on a noisy channel.
C = B × log₂ (1 + SNR)
  C = channel capacity (bits per second)
  B = bandwidth of the channel (Hz)
  SNR = signal-to-noise ratio (as a plain ratio, not dB)
Formulated by Claude Shannon in 1948; sets an upper bound regardless of the signal levels used.
Increasing bandwidth or improving SNR both raise the maximum achievable capacity.
Channel Capacity